## Slide 1: Chapter 1 Binary Systems
Pooja Thakkar
Assistant Professor, CE/IT
U. V. Patel College of Engineering(UVPCE), Ganpat University

## Slide 2: Outline of Chapter 1
Digital Computers and Digital Systems
Binary Numbers
Number-base Conversions
Octal and Hexadecimal Numbers
Complements
Signed Binary Numbers
Binary Codes
Binary Storage and Registers
Binary Logic

## Slide 3: Block Diagram of Digital Computer

## Slide 4: Binary Digital Signal
A digital signal is a signal that is being used to represent data as a sequence of discrete values
These values are binary values
Binary values are represented abstractly by:
  0 and 1
  False (F) and True (T)
  Low (L) and High (H)
  On and Off

## Slide 5: Number Systems

## Slide 6: Number Base Conversions
Decimal to Binary
Decimal to Octal
Decimal to Hexadecimal
Binary to Decimal
Octal to Decimal
Hexadecimal to Decimal
Binary to Hexadecimal
Hexadecimal to Binary
Binary to Octal
Octal to Binary
Octal to Hexadecimal
Hexadecimal to Octal

## Slide 7: Decimal to Binary
2
1
6
0
2
2
1
3
1
13

## Slide 8: Decimal to Binary
 | 10 | 
2
0
5
1
2
2
1
2
0
Fractional Part:
0.25 * 2 = 0.50
0.50 * 2 = 1.00

## Slide 9: Decimal to Binary
(32
(52.25

## Slide 10: Decimal to Binary
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
0011
0001
0010
0000
0100
0101
0110
0111
1000
1001
1010
1101
1100
1011
1110
1111
20
21
22
23
20
21
22
23

## Slide 11: Decimal to Octal
(105)10
= (151)8
 | 105 | 
8
1
13
8
1
5

## Slide 12: Decimal to Octal
(10.25)10
Fractional Part:
0.25*8 = 2.00
(10)10 = (12)8
= (12.2)8
 | 10 | 
8
2
1

## Slide 13: Decimal to Octal
(37)10
(255.5)10
= (45)8
= (377.4)8

## Slide 14: Decimal to Hexadecimal
(86)10
= (56)16
 | 86 | 
16
6
5
0 to 9 & A to F

## Slide 15: Decimal to Hexadecimal
(193)10
= (C1)16
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F
 | 193 | 
16
1
12

## Slide 16: Decimal to Hexadecimal
(1271.37)10
Fractional Part:
0.37*16 = 5.92
0.92*16 = 14.72
0.72*16 = 11.52
0.52*16 = 8.32…
(1271)10 = (4F7)16
 | 1271 | 
16
7
79
16
4
15
(0.37)10 = (5EB8..)16
= (4F7.5EB8..)16

## Slide 17: Decimal to Hexadecimal
(37)10
(255.5)10
= (25)16
= (FF.8)16

## Slide 18: Binary to Decimal
(1101)2
1
1
0
1
20
21
22
23
= 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20
= 8 + 4 + 0 + 1
= (13)10

## Slide 19: Binary to Decimal
(1010.01)2
1
0
1
0
20
21
22
23
= 1x23 + 0x22 + 1x21 + 0x20 + 0x2-1 + 1x2-2
= 8 + 0 + 2 + 0 + 0 + 0.25
= (10.25)10
0
2-1
1
2-2

## Slide 20: Binary to Decimal
(10101)2
(1111.11)2
= (21)10
= (15.75)10

## Slide 21: Octal to Decimal
3
7
80
81
(37)8
= 3 x 81 + 7 x 80
= 24 + 7
= (31)10

## Slide 22: Octal to Decimal
1
2
80
81
2
8-1
(12.2)8
= 1 x 81 + 2 x 80 +2 x 8-1
= 8 + 2 + 2(0.125)
= (10.25)10

## Slide 23: Octal to Decimal
(76)8
(41.26)8
= (62)10
= (33.34375)10

## Slide 24: Hexadecimal to Decimal
1
2
161
162
10
160
(12A)16
= 1 x 162 + 2 x 161 + 10 x 160
= 256 + 32 + 10
= (298)10

## Slide 25: Hexadecimal to Decimal
(AD2.4)16
10
13
2
1
16-1
160
161
162
= 10 x 162 + 13 x 161 + 2 x 160 + 4 x 16-1
= 2560 + 208 + 2 + 0.25
= (2770.25)10

## Slide 26: Hexadecimal to Decimal
(76)16
(4A.26)16
= (118)10
= (74.1484375)10

## Slide 27: Octal to Binary
(67)8
(25)8
(42.254)8
= ( )2
110
111
= ( )2
010
101
= (100010.0101011)2
= ( . )2
100
010
010
101
100
= (10101)2

## Slide 28: Binary to Octal
(111101)2
(11101)2
(1101101.11011)2
= ( )8
5
7
= (011101)2
= ( )8
5
3
= (001101101.110110)2
= (155.66)8

## Slide 29: Hexadecimal to Binary
(F8)16
(A21.A4)16
(12.4)16
= ( )2
1111
1000
= ( . )2
1010
0010
0001
1010
0100
= ( . )2
0001
0010
0100
= (101000100001.101001)2
= (10010.01)2

## Slide 30: Binary to Hexadecimal
(1101101101111.01001011)2
( )2
1111
0011
0010
= (F32)16
( . )2
1001
0001
0010
1001
1100
= (912.9C)16
= (0001101101101111.01001011)2
= (1B6F.4B)16

## Slide 31: Hexadecimal to Octal
(A1)16
(F2.01)16
Hexadecimal to Binary
Binary to Octal
= (10100001)2
= (010100001)2
= (241)8
= (11110010 . 00000001)2
= (011110010 . 000000010)2
= (362.002)8

## Slide 32: Octal to Hexadecimal
(573)8
(1.01)8
Octal to Binary
Binary to Hexadecimal
= (101111011)2
= (000101111011)2
= (17B)16
= (001.000001)2
= (0001.00000100)2
= (1.04)16

## Slide 33: Number Base Conversions
Decimal to Binary
Decimal to Octal
Decimal to Hexadecimal
Binary to Decimal
Octal to Decimal
Hexadecimal to Decimal
Binary to Hexadecimal
Hexadecimal to Binary
Binary to Octal
Octal to Binary
Hexadecimal to Octal
Octal to Hexadecimal

## Slide 34: Arithmetic Operations on Binary Numbers
Binary Addition
Binary Subtraction
Binary Multiplication
Binary Division

## Slide 35: Binary Addition
1 1 0 1 1 1
+ 1 0 1 0 1 0
A | B | Carry | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 36: Binary Addition
1 1 1 1 0 1
+ 1 0 1 1 1
1 1 1 1 1 1
+ 1 1 1 0 1 1

## Slide 37: Binary Addition
1 1 1 . 1 0 1
+ 1 1 0 . 1 1 1
1 0 1 1 0 1 . 1 0 1
+ 1 1 1 0 1 . 1 0 1

## Slide 38: Binary Subtraction
1 1 0 0 1
- 1 0 1 0 1
A | B | Difference | Borrow
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0

## Slide 39: Binary Subtraction
1 0 0 1 1 0 1
- 1 0 1 1 1
1 0 0 1 0 1
- 1 1 0 1 0

## Slide 40: Binary Subtraction
1 1 1 . 0 1
- 1 0 1 . 1 0
1 0 0 1 1 0 1 . 0 1 0
- 1 1 0 1 0 1 . 1 1 1

## Slide 41: Binary Multiplication
1 0 1 1 1
* 1 0 1 0
1 0 1 1 1 0 0 0
0 0 0 0 0 0 0
1 0 1 1 1 0
0 0 0 0 0
A | B | Multiply
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0
1
1
0
0
1
1
1

## Slide 42: Binary Multiplication
1 1 0 1 1
* 1 0 1
1 0 1 1 0 1
* 1 1 0 1

## Slide 43: Binary Division
1 1 1 1 1
1 0 0
1
1
1
1 0 0
0 1 1
1
1 0 0
0 1 1
1
1 0 0
0 1 1
1 0 0 1 0 1 1 1
1 0 1

## Slide 44: Complements
There are two types of complements for each base-r system:
  Diminished radix complement - (r-1)’s Complement
  Radix complement - r’s Complement

## Slide 45: 1’s Complement
00100 
10010111 
100101.010 

## Slide 46: 2’s Complement
1101101 
10101 
1001001.01 
101.101 

## Slide 47: 10’s Complement
Formula - (rn - N)
r = Base of Number system, n = No. of digits, N = Number to be find complement of
(239)10
  r = 10 , n = 3, N = 239
  = - 239
  = 1000 – 239 = 761
(012398)10

## Slide 48: 10’s Complement
(0.235)10
  r = 10 , n = 0, N = 0.235
  - 0.235
  0 – 0.235 = 0.765
(52.125)10
  r = 10 , n = 2, N = 52.125
  - 52.125
  100 – 52.125 = 47.875

## Slide 49: 9’s Complement
Formula - (rn – r-m) – N
r = Base, n = int no. of digits, m = float no. of digits, N = Number
(239)10
  r = 10, n = 3, m = 0, N = 239
  (103 – 10-0 – 239)
  1000 – 1 – 239 = 760
(521)10

## Slide 50: 9’s Complement
(37.135)10
  r = 10, n = 2, m = 3, N = 37.135
  (102 - 10-3 - 37.135)
  100 - 0.001 - 37.135 = 62.864
(0.375)10
  r = 10, n = 0, m = 3, N = 0.375
  (100 - 10-3 – 0.375)
  1 - 0.001 – 0.375 = 0.624

## Slide 51: Subtraction with Complements
The subtraction of two n-digit unsigned numbers M – N in base r can be done as follows:

## Slide 52: Subtraction using 10's complement
69245 – 14258
Find 10’s complement of 14258 =
Add 69245 and 85742
Discard the carry
6 9 2 4 5
8 5 7 4 2
+
85742
= 54987
1 5 4 9 8 7

## Slide 53: Subtraction using 10's complement
2. 72532 – 3250
Find 10’s complement of 03250 =
Add 72532 and 96750
Discard the carry
7 2 5 3 2
9 6 7 5 0
+
96750
= 69282
1 6 9 2 8 2

## Slide 54: Subtraction using 10's complement
3. 2341 – 4237
Find 10’s complement of 4237 =
Add 2341 and 5763
As no carry is generated, find 10’s complement of 8104 =
2 3 4 1
5 7 6 3
+
5763
= -1896
1896
8 1 0 4

## Slide 55: Subtraction using 10's complement
4. 3250 – 72532
Find 10’s complement of 72532 =
Add 3250 and 27468
As no carry is generated, find 10’s complement of 30718 =
0 3 2 5 0
2 7 4 6 8
+
27468
= -69282
69282
3 0 7 1 8

## Slide 56: Subtraction using 2's complement
1. 1010100 - 1000011
Find 2’s complement of 1000011 =
Add 1010100 and 0111101
Discard the carry
1 0 1 0 1 0 0
0 1 1 1 1 0 1
+
0111101
= 10001
1 0 0 1 0 0 0 1

## Slide 57: Subtraction using 2's complement
2. 1000011 – 1010100
Find 2’s complement of 1010100 =
Add 1000011 and 0101100
As no carry is generated, find 2’s complement of 1101111 =
1 0 0 0 0 1 1
0 1 0 1 1 0 0
+
0101100
= -10001
1 1 0 1 1 1 1
0010001

## Slide 58: Subtraction with Complements
Subtraction of unsigned numbers can also be done by means of the (r  1)'s complement. Remember that the (r  1) 's complement is one less then the r's complement.

## Slide 59: Subtraction using 9's complement
1. 54326 – 8235
Find 9’s complement of 08235 =
Add 54326 and 91764
Add the carry to the answer
5 4 3 2 6
9 1 7 6 4
+
91764
= 46091
1 4 6 0 9 0
4 6 0 9 0
1
+
4 6 0 9 1

## Slide 60: Subtraction using 9's complement
2. 54231 – 82345
Find 9’s complement of 82345 =
Add 54231 and 17654
As no carry is generated, find 9’s complement of 71885 =
5 4 2 3 1
1 7 6 5 4
+
17654
= -28114
7 1 8 8 5
28114

## Slide 61: Binary Codes
The digital data is represented, stored and transmitted as group of binary bits.
This group is also called as binary code.
The binary code is represented by the number as well as alphanumeric letter.

## Slide 62: BCD Code
In this code each decimal digit is represented by a 4-bit binary number. BCD is a way to express each of the decimal digits with a binary code.
A decimal number in BCD is the same as its equivalent binary number only when the number is between 0 and 9.
The binary combinations 1010 through 1111 are not used and have no meaning in BCD.

## Slide 63: BCD Code

## Slide 64: BCD Code
Example:
  =

## Slide 65: Gray Code
Reflected Code
The advantage is that only bit in the code group changes in going from one number to the next.
  Error detection.
  Representation of analog data.
  Low power design.
000
001
010
100
110
111
101
011

## Slide 66: Excess 3 Code
It is a self-complementary binary coded decimal (BCD) code.
We need to add 3 to both digit in the decimal number then convert into BCD

## Slide 67: Excess 3 Code
Example:
  =

## Slide 68: ASCII Codes
American Standard Code for Information Interchange
A popular code used to represent information sent as character-based data.
It uses 7-bits to represent:
  94 Graphic printing characters.
  34 Non-printing characters.
Some non-printing characters are used for text format (e.g. BS = Backspace, CR = carriage return).
Other non-printing characters are used for record marking and flow control (e.g. STX and ETX start and end text areas).

## Slide 69: Error-Detecting Code
To detect errors in data communication and processing, an eighth bit is sometimes added to the ASCII character to indicate its parity.
A parity bit is an extra bit included with a message to make the total number of 1's either even or odd.
Example:
  Consider the following two characters and their even and odd parity:

## Slide 70: Signed Binary Numbers
The convention is to make the
  sign bit 0 for positive and
  1 for negative.