## Slide 1: Combinational Logic
Pooja Thakkar
Assistant Professor, CE/IT
U. V. Patel College of Engineering(UVPCE), Ganpat University

## Slide 2: Introduction
Consists of logic gates whose outputs, at any time, are determined by combining the values of the inputs.
For n input variables, there are 2n possible binary input combinations.
For each binary combination of the input variables, there is one possible output.

## Slide 3: Introduction
Hence, a combinational circuit can be described by:
  A truth table that lists the output values for each combination of the input variables, or
  m Boolean functions, one for each output variable.

## Slide 4: Introduction
Combinational
Circuit
n-inputs
m-outputs
(Depend only on inputs)
Combinational
Circuit
n-inputs
m-outputs
Storage
Elements
Next
state
Present
state
Sequential Circuit
Combinational Circuit

## Slide 5: Design Procedure
State the problem.
Determine the required number of inputs and outputs and assign a symbol to each.
Derive the truth table that defines the required relationship between inputs and outputs.
Obtain the simplified Boolean functions for each output.
Draw the logic diagram.

## Slide 6: Adders
The most basic arithmetic operation is the addition of two binary digits.
Combination circuit that performs the addition of two bits is half adder
Adder that performs the addition of 2 significant bits and a previous carry is called a full adder

## Slide 7: Half adder
Inputs: x and y
Outputs: S (for sum) and C (for carry)
x | y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
S = x’y + xy’
C = xy

## Slide 8: Implementation of a Half Adder

## Slide 9: Full Adder
x | y | z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
C

## Slide 10: Implementation of a Full Adder
C= xy + xz +yz
S = x ' y ' z + x 'yz ' + xy ' z ' +xyz

## Slide 11: Implementation of a Full Adder
A full adder can be implemented with two half adders and an OR gate
S = xy’z’ + x’yz’ + xyz + x’y’z
= z’(xy’ + x’y) + z(xy’ + x’y)’
= z ⊕ (x ⊕ y)
C = xy’z + x’yz + xy
= z(xy’ + x’y) + xy

## Slide 12: 4-bit Binary Adder
Consider two binary number
A = 1011 and B = 0011

## Slide 13: 4-bit Binary Adder

## Slide 14: Carry Propagation
In parallel adder, for each adder block, the two bits that are to be added are available instantly.
However, each adder block waits for the carry to arrive from its previous block.
So, it is not possible to generate the sum and carry of any block until the input carry is known. That is block waits for the block to produce its carry.
So there will be a considerable time delay which is called as carry propagation delay.

## Slide 15: Carry Propagation
The propagation time is equal to the propagation delay of each adder block, multiplied by the number of adder blocks in the circuit.
For example, if each full adder stage has a propagation delay of 20 nanoseconds, then will reach its final correct value after 60 (20 × 3) nanoseconds. The situation gets worse, if we extend the number of stages for adding more number of bits.

## Slide 16: Look-ahead Carry Generator
Pi = Ai ⊕ Bi
Gi = AiBi
Output sum and carry
Si = Pi ⊕ Ci
Ci+1 = Gi + PiCi
Gi : carry generate Pi : carry propagate
C0 = input carry
C1 = G0 + P0C0
C2 = G1 + P1C1 = G1 + P1G0 + P1P0C0
C3 = G2 + P2C2 = G2 + P2G1 + P2P1G0 + P2P1P0C0
C3 does not have to wait for C2 and C1 to propagate.

## Slide 17: Look-ahead Carry Generator

## Slide 18: 4-bit Full-adder with look-ahead carry

## Slide 19: Half Subtractor
Diff = A’B+AB’
Borrow = A’B

## Slide 20: Full Subtractor
One that performs the subtraction of three bits is a full subtractor.

## Slide 21: Full Subtractor
D = A’B’C+A’BC’+AB’C’+ABC
C = A’C+A’B+BC

## Slide 22: Full Subtractor

## Slide 23: Full Subtractor
Full-subtractor can also be implemented with two half subtractor and one OR gate.

## Slide 24: 4-bit Adder-Subtractor
K=0 (Adder)
  Input of FA is A and B (B 0 = B), and C0 is 0
K=1 (Subtractor)
  Input of FA is A and B' (B 1 = B'), and C0 is 1

## Slide 25: BCD Adder
BCD adder
  Perform the addition of two decimal digits in BCD, together with an input carry from a previous stage
BCD adder requires minimum of 9 inputs & 5 outputs
  1 digit requires 4-bit
  Input: 2 digits + 1-bit carry
  Output: 1 digit + 1-bit carry
  The output sum cannot be greater than 19 (9+9+1)

## Slide 26: BCD Adder
When the binary sum is equal to or less than 1001 in Binary
  BCD Sum = Binary Sum
  C = 0
When the binary sum is greater than 1001 in Binary
  BCD Sum = Binary Sum + 0110b
  C = 1

## Slide 27: BCD Adder

## Slide 28: BCD Adder
1 | 1 | 1 | 1
 |  | 1 | 1

## Slide 29: BCD Adder Implementation
If C =1 , it is necessary
to add 0110 to binary sum
C = K + Z8Z4 + Z8Z2

## Slide 30: Magnitude Comparator
Combinational circuit that compares two digital or binary numbers and find out whether one number is equal, less than or greater than the other number.
3 binary variables are used to indicate the outcome as A>B, A<B, or A=B.

## Slide 31: 4 Bit Magnitude Comparator
Equal (A = B)
  = and = and = and =
  (A = B) All 1’s i.e X3X2X1X0
Greater (A > B) or Less (A < B)
  Comparison start from the MSB
  If the two digits are equal, compare next lower digits
  Continues until a pair of unequal digits is reached
    A is 1 and B is 0 => A > B
    A is 0 and B is 1 => A < B
Xi = AiBi + Ai'Bi' for i = 0,1,2,3
(A > B) = A3B3' + X3A2B2'+ X3X2A1B1' + X3X2X1A0B0'
(A < B) = A3'B3 + X3A2' B2+ X3X2A1' B1 + X3X2X1A0' B0

## Slide 32: 4 Bit Magnitude Comparator

## Slide 33: 4 Bit Magnitude Comparator

## Slide 34: Decoder
Combinational circuit that has,
  n input lines and
  maximum of output lines.
One of these outputs will be active High based on the combination of inputs present, when the decoder is enabled.
That means decoder detects a particular code.

## Slide 35: 2 x 4 Decoder
EN | A | B | Y0 | Y1 | Y2 | Y3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
Y0
Y1
Y2
Y3
EN

## Slide 36: 2 x 4 Decoder

## Slide 37: 3 x 8 Decoder
EN | A | B | C | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
0 | X | X | X | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7

## Slide 38: 3 x 8 Decoder

## Slide 39: 4 x 16 Decoder
D | A | B | C | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10 | Y11 | Y12 | Y13 | Y14 | Y15
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 40: 4 x 16 Decoder

## Slide 41: 5 x 32 Decoder

## Slide 42: Example
Implement full adder circuit with a decoder and two OR gate.
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S(X,Y,Z) =
C(X,Y,Z) =

## Slide 43: Encoder
Combinational circuit that performs the reverse operation of Decoder.
  input lines and
  ‘n’ output lines.
It will produce a binary code equivalent to the input, which is active High. Therefore, the encoder encodes input lines with ‘n’ bits.
The process of converting from familiar symbols or numbers to a coded format is called encoding.

## Slide 44: Encoder

## Slide 45: 4 x 2 Encoder
Inputs |  |  |  | Outputs | 
1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1
Inputs |  |  |  | Outputs | 
1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1

## Slide 46: 4 x 2 Encoder

## Slide 47: 8 x 3 Encoder
Inputs |  |  |  |  |  |  |  | Outputs |  | 
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
Inputs |  |  |  |  |  |  |  | Outputs |  | 
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1

## Slide 48: 8 x 3 Encoder

## Slide 49: Multiplexer
Circuit that has multiple inputs and a single output.
Selection of one of ‘n’ inputs is done by select lines
It has one output selected at a time.
Also known as DATA SELECTOR.
A multiplexer has
- N data inputs (multiple)
- 1 output (single)
- M select inputs, with 2M =N

## Slide 50: Block Diagram of Multiplexer

## Slide 51: 2 to 1 line Multiplexer
Y=D0S’+D1S

## Slide 52: 4 to 1 line Multiplexer
Y=S1’S0’D0+S1’S0D1+S1S0’D2+S1S0D3

## Slide 53: 8 to 1 line Multiplexer
Y=S2’S1’S0’D0+S2’S1’S0D1+S2’S1S0’D2+S2’S1S0D3
+S2S1’S0’D4+S2S1’S0D5+S2S1S0’D6+S2S1S0D7

## Slide 54: 8 to 1 line Multiplexer
Y
S2
S1
S0

## Slide 55: Examples
Implement following function with a Multiplexer.
F(A,B,C) =
Minterm | A | B | C | F
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 1
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 1
6 | 1 | 1 | 0 | 1
7 | 1 | 1 | 1 | 0
 | D0 | D1 | D2 | D3
A’ | 0 | 1 | 2 | 3
A | 4 | 5 | 6 | 7

## Slide 56: Examples
Implement following function with a Multiplexer. Keep A,B as Selection lines and use 4*1 Multiplexer
F(A,B,C) =
Minterm | A | B | C | F
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | 1
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 1
5 | 1 | 0 | 1 | 1
6 | 1 | 1 | 0 | 0
7 | 1 | 1 | 1 | 0
 | D0 | D1 | D2 | D3
C’ | 0 | 2 | 4 | 6
C | 1 | 3 | 5 | 7

## Slide 57: Examples
Implement following function with a Multiplexer.
F(A,B,C,D) =
 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
A’ | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
A | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 58: De-multiplexer
Combinational Circuit with one input and multiple output lines.
Types :
  1 to 2 Line De-multiplexer (Selection lines = 1)
  1 to 4 Line De-multiplexer (Selection lines = 2)
  1 to 8 Line De-multiplexer (Selection lines = 3)

## Slide 59: 1 to 8 line De-multiplexer